## Slide 1
The always-on nature of VAs triggers misactivation!
Enhancing Security and Privacy Control for Voice
Assistants Using Speaker Orientation
Shaohu Zhang
szhang42@ncsu.edu
Motivation
VAs can be misactivated by suboptimal wakeword and background chat.
Visual gaze plays an important role in interpersonal communication. People tend to look at each other when chatting.
We propose a device-free and non-obtrusive acoustic sensing system called HeadTalk, a speaker orientation–aware privacy control approach.
More detail to download the full draft of the paper
Human Field-of-View ( FoV )
HeadTalk privacy control vs. Natural mode vs. Mute button mode. HeadTalk mode detects the presence of the wake word, and if spoken while facing the VA, it continues to operate in normal mode, otherwise it mutes the microphones
Speech Propagation
Evaluation
Experiment across three prototypes
1
3 devices: UMA-8 USB mic array, ReSpeaker Core v2.0, and ReSpeaker USB mic array;
3 wake words: "Hey Assistant!", "Computer" and "Amazon";
3 different time frame: day, week and month;
2 rooms: lab and home;
3 distances: 1 meter, 3 meters and 5 meters;
14 angles: 0◦, +15◦, -15◦, +30◦, -30◦, +45◦, -45◦, +60◦, -60◦, +90◦, -90◦, +135◦, -135◦, 180◦.
Overall Accuracy
Takeaway
Voice Command can be used to sense head orientation for privacy control
Potential to make distributed voice interactions more practical and secure
System Design
Speech propagation FoV in the horizontal plane. 35 degree on both sides of the centerline is referred to as the immediate FoV
Higher magnitude in the forward direction compared to the backward direction
Aafaq Sabir
asabir2@ncsu.edu
Anupam Das
anupam.das@ncsu.edu
Speaker
Directed
Propagation
Microphone
Array
Reverberation
Lab and home setup
Performance of different devices
HeadTalk consists of two main components including liveness detection and speaker orientation recognition. HeadTalk only accepts the wakeword when the user is facing the device.
Generalized Cross Correlation with Phase Transform (GCC-PHAT)
Steered Response Power with Phase Transform (SRP-PHAT)
Performance of different environments